## Slide 1: GFM Autotuning

## Slide 2: Inputs
Required imputed
maxTrq maximum allow torque
maxVel maximum positive speed
maxPos maximum positive position
minVel maximum negative speed
minPos maximum negative position;
phi_m_v speed loop phase margin (now 75°)
MinWc minimum value of the controller bandwidth
MaxWc maximum value of the controller bandwidth
pOscillationTollerance allow torque oscillation tolerance, torque standard deviation will be smaller than maxTrq*pOscillationTollerance (now 0.3)
pLow_Vel_Thr threshold between low- and high-speed conditions.

## Slide 3: Autotuning states
State 0: Noise Level Identification
  Description: Identify velocity noise. The motor does not move, noise is the maximum absolute value of the velocity
  Control mode: torque
  Transitions: to state TimeId (default: 1.0) seconds.
State 1: Static friction identification
  Description: Identify static friction (namely, the Coulomb coefficient). The torque is increased until the motor start to move.
  Control mode: torque
  Transitions: to state 1 for friction_trial times, then go to state 2.

## Slide 4: Autotuning states
State 2: Inertia identification
  Description: Identify viscous friction coefficient and the motor inertia. The motor moves in positive and negative directions.
  Control mode: torque
  Transitions: to state 1 after Time_identification (default: 7.0) seconds.
State 3: Inertia identification - stopping
  Description: stop motor after identification.
  Control mode: torque
  Transitions:
    to state 4 if the identified parameters are correct setting the bandwidth equal to the minimum value
    to state 100 otherwise.

## Slide 5: Autotuning states
State 100: reset to wrong model identification
  Description: reset the autotuner and repeat identification
  Control mode: torque
  Transitions: to state 0 if estimation_trials is less than 3, otherwise go to state 92.
State 4: tuning at low-speed levels
  Description: update low-speed controller parameters and switch to speed mode.
  Control mode: torque
  Transitions: to state 5 when the parameters have been updated

## Slide 6: Autotuning states
State 5: stop movements
  Description: ensure that the motor is stopped
  Control mode: speed
  Transitions: to state 6 after TrialTime (default: 2.0) seconds, or 0.2*TrialTime seconds if the speed is smaller than the noise level. Set velocity setpoint to a random value, smaller than the threshold between low and high velocity (maxVel*low_vel_thr)
State 6: rise time
  Description: compute the rise time at 95% of the setpoint value.
  Control mode: speed
  Transitions:
    to state 7 when speed reach 95% of the setpoint
    To state 9 if the speed overshoot is greater than 30%.

## Slide 7: Autotuning states
State 7: waiting steady state
  Description: wait the end of the transient
  Control mode: speed
  Transitions:
    to state 8 after min(0.4*TrialTime,3.0*rise time) seconds.
    To state 9 if the speed overshoot is greater than 30%.

## Slide 8: Autotuning states
State 8: computing variance
  Description: compute torque variance and standard deviation SIGMA
  Control mode: speed
  Transitions:
    to state 4 after min(0.7*TrialTime,5.0*rise time) seconds If the standard deviation SIGMA is smaller than the threshold and the control bandwidth is smaller than the maximum value, increasing the controller bandwidth
    To state 9 after min(0.7*TrialTime,5.0*rise time) seconds If the standard deviation SIGMA is greater than the threshold and the control bandwidth is greater than the maximum value. Change to high speed tuning, set bandwidth equal to the minimum value
State 9: tuning at high-speed levels
  Description: update high-speed controller parameters
  Control mode: speed
  Transitions: to state 5 when the parameters have been updated

## Slide 9: Autotuning states
State 10: stop movements
  Description: ensure that the motor is stopped
  Control mode: speed
  Transitions: to state 11 after TrialTime (default: 2.0) seconds, or 0.2*TrialTime seconds if the speed is smaller than the noise level. Set velocity setpoint to a random value, greater than the threshold between low and high velocity (maxVel*low_vel_thr)
State 11: rise time
  Description: compute the rise time at 95% of the setpoint value.
  Control mode: speed
  Transitions: Transitions:
    to state 12 when speed reach 95% of the setpoint
    To state 9 if the speed overshoot is greater than 30%.

## Slide 10: Autotuning states
State 12: waiting steady state
  Description: wait the end of the transient
  Control mode: speed
  Transitions:
    to state 8 after min(0.4*TrialTime,3.0*rise time) seconds.
    To state 9 if the speed overshoot is greater than 30%.

## Slide 11: Autotuning states
State 13: computing variance
  Description: compute torque variance and standard deviation SIGMA
  Control mode: speed
  Transitions:
    to state 9 after min(0.7*TrialTime,5.0*rise time) seconds If the standard deviation SIGMA is smaller than the threshold and the control bandwidth is smaller than the maximum value, increasing the controller bandwidth
    To state 14 after min(0.7*TrialTime,5.0*rise time) seconds If the standard deviation SIGMA is greater than the threshold and the control bandwidth is greater than the maximum value.
State 9: save tuning at high-speed levels
  Description: update high-speed controller parameters
  Control mode: speed
  Transitions: to state 15 when the parameters have been updated

## Slide 12: Autotuning states
State 15: tuning completed
  Description: tuning completed, final state.
  Control mode: speed
  Transitions: NONE
State 91: velocity tracking error
  Description: unable to reach steady state during the tuning phase
  Control mode: speed
  Transitions: NONE
State 92: parameter identification error
  Description: unable to identify the model
  Control mode: torque
  Transitions: NONE

## Slide 13: Autotuning states
State 99: constraints violation
  Description: constraints violation
  Control mode: speed/torque
  Transitions: NONE

## Slide 14: Test in HIL
Estimated friction compared to the HIL value
COMPLETE TEST CAMPAIN

## Slide 15: Relation between constraints amplitude and identified model
Coulomb friction
Coulomb friction requires multiple test to having a correct estimation.

## Slide 16: Relation between constraints amplitude and identified model
Inertia
Low speed and low torques reduces estimation accuracy.

## Slide 17: Relation between constraints amplitude and identified model
Viscous friction
Low speed and low torques reduces estimation accuracy.
It depends on the accuracy of Coulomb friction identification